## Slide 1: ASIC² Research Group Project: Design of peripheral circuit of memory array to perform in-memory logic operations
Background: A memristive device (or a ‘memristor’ in short) is a two-terminal device whose resistance is determined by an internal state, which can be varied by the application of a voltage/current. The capability to toggle resistance (between a Low Resistance State - LRS, and a High Resistance State- HRS) in response to voltage/current is perhaps the most desirable property of memristors, extending their use from memory to computing. They are promising candidates for in-memory computing to solve the von-neumann bottleneck. MAGIC1(Memristor Aided logic) is a memristive logic family which can be used to implement in-memory computing. Combinational logic can be executed in the memory array efficiently using MAGIC logic family.
Project Description:
The conventional memory used for storage needs a peripheral circuitry(consisting of row decoders, voltage controllers, sense amplifiers) that only supports memory read/write operations. The peripheral circuit of the memory(2D array of memristors) has to be modified/enhanced to support logic operations while still supporting the memory operations. The enhancements should include:
i)The ability to select multiple rows/columns to enable more parallel execution of logic operations.
ii) The ability to apply additional distinct voltages beyond the voltages used for memory operation (VREAD, Vwrite etc).
The peripheral circuit should be energy efficient. In this project, the student is expected to design this modified peripheral circuit which can support logic operations in large arrays(512x512, 1024x1024) efficiently.
Links
Contacts Details: John Reuben, post-doc (johnreubenp@gmail.com)
Lab Details: ASIC2 lab, TCE 408
1 S. Kvatinsky, D. Belousov, S. Liman, G. Satat, N. Wald, E. G. Friedman, A. Kolodny, and U. C. Weiser, “MAGIC- Memristor-Aided loGIC,” IEEE Transactions on Circuits and Systems II: Express Briefs, vol. 61, no. 11, pp. 895–899, Nov 2014